Section:Raster Analysis
Module : Clipping Rasters

 Clipping rasters with QGIS
“QGIS provides various ways to clip a raster layer. In this worksheet we will look at one approach.”
If you have a raster that is larger than the area needed for your map or analysis, you can clip it to a smaller size using QGIS. In addition you can ‘mask’ the layer using a polygon in order to assign no data values to pixels outside of your target area.

You try:
Goal: To clip a subset of raster data using a polygon
* Load the two datasets indicated in the table right.
* Select one district and use the ‘save as’ option to save just that district to a new shapefile.
* Remove the original districts layer.
* Use the Raster -> Extract -> Clip tool to clip the population dataset using the district.

Name	Value
Data	appendix3-local-data/kzn_pop_count.tif
	appendix3-local-data/districts.shp

More about raster clipping
Raster data contains cells which are organised into rows and columns where each cell contains values representing information. Because raster images are generally very big and contains a lot of pixels (information) it is sometimes imperative to clip them . This can be achieved by either using a shapefile as a mask layer or by specifying an extent.
When clipping a raster layer we can change the other characteristics of the output layer like nodata values,spatial resolution and adding an alpha band to the output raster.
The spatial resolution of a raster defines the smallest possible feature that can be detected. Nodata values are used to represent areas of a raster that have no data or areas in the raster that you do not want to show based on the pixel values in the raster.
An alpha band acts as a transparency mask,providing a transparency value for each pixel.

Check your knowledge:
Clipping rasters with QGIS is done either by rectangle or by a polygon layer:
1. true
2. false
Which statement is true:
1. You only use a mask layer to clip a raster when the shape of the mask is an irregular polygon.
2. Raster images where large features are visible are defined as having low resolution.
3. Clipping alters the pixel values in the raster.
The nodata values of raster can only be defined as 0:
- True
- False

Further reading:

https://docs.qgis.org/2.14/en/docs/training_manual/processing/cutting_merging.html
http://www.qgistutorials.com/en/docs/raster_mosaicing_and_clipping.html