Section:Raster
Module :Georeferencing

Georeferncing in Context
“ Georeferencing is the process of assigning real world coordinates to a map so that it draws in it’s actual position”
In this module we will learn how to georeference old scanned maps in QGIS. The maps are usually old topographic sheets or maps which are scanned to be used in a GIS or any other raster layer that have no geographic information. You cannot overlay other layers with a raster that has not been georeferenced.

You try:
Goal: To learn how to georeference a scanned map. This will enable overlay with other existing layers in the same CRS or different CRS
* Add vector layer from natural earth data. Add a roads/building layers to use as reference. Lesotho is a country close to South Africa
* Enable on the fly projection
* Activate georeference from plugins.
* Open the raster and specify the CRS for the layer
* Digitize the raster and choose adequate control points and ensure the residuals are as low as possible
Check your results:
Once you have finished georeferencing export the raster and it should overlay the layers loaded in QGIS

Name	Value
CRS	4326
Reference Layer	Vector from natural earth
Raster Operation	Georeferencing
Operation	On the fly projection
Raster	Lesotho.jpg

More about
It is important to understand that when you georeference a map you should use the projection that is specific to the area from which your map has come from. Georeferencing when done correctly will enable layers with different projections to be overlay together when on the fly projection is activated.

Check your knowledge:
Georeferencing allows us to:
1. Assign real world coordinates to a map
2. Enable map layers to be overlaid together once a raster image has been georeferenced.
3. Only raster layers can be georeferenced.

Further reading:
 https://docs.qgis.org/2.14/en/docs/training_manual/forestry/map_georeferencing.html
 https://www.ordnancesurvey.co.uk/support/understanding-gis/georeferencing.html
http://www.qgistutorials.com/en/docs/advanced_georeferencing.html